## Slide 1: Restoring Division Algorithm
Abdullah Nadeem
2023-EE-126
Introduction and Concept.
Umair Nadeem
2023-EE-115
Topic: How the Algorithm works.
Abdul Nafeh
2023-EE-124
Topic: Example of The Working.
Azaan Shah Tirmazi
2023-EE-129
Topic: Applications of Restoring Division.

## Slide 2: What is Restoring Division?
A method to mimic binary long division
“Restores” the value if the subtraction goes negative.
Used in Various ALUs.
Involves shifting and subtracting
  Shifts bit to align
  Subtract Divisor
  If Negative, Restore

## Slide 3: Restoring Vs Non-Restoring
Restoring
Slower since there is a restoring operation.
Higher per step complexity.
Less efficient.
Easier to understand and implement.
Non-Restoring
Faster since there is no restoring.
Lower per step complexity.
More efficient.
Harder to understand and implement.

## Slide 4: Key Components
Dividend (Q) : The number to be divided (size N)
Divisor (M) : The number dividing/denominator (size N+1)
Remainder(A): Initially set to 0,stores intermediate results (size N+1)
Counter : Tracks the number of bits (size N)

## Slide 5: Step-by-Step Algorithm
Initialization :
A = 0 (Remainder register cleared)
Q = Dividend (Loaded into the quotient register)
M = Divisor(Stored in a separate register).
Counter = n (Number of bits in Q)

## Slide 6: Steps for each Iteration:
Step 1: Left-Shift AQ
A and Q are combined and shifted left by 1 bit.
The MSB of Q moves into the LSB of A.
The LSB of Q is filled with 0 (temporarily).
Example:
Before: A = 0000, Q = 0111
After Shift: A = 0000, Q = 1110
Step 2: Subtract M from A
A = A – M
If A becomes negative, the subtraction was invalid.
If A ≥ 0, the subtraction was valid.

## Slide 7
Step 3: Check MSB of A
Case 1: A[n] = 1 (Negative)
Restore A by adding M back: A = A + M.
Set LSB of Q to 0 (since subtraction failed).
Case 2: A[n] = 0 (Positive or Zero)
Set LSB of Q to 1 (subtraction was successful).
Step 4: Decrement Counter
Repeat until all bits are processed.
Final Result
Quotient (Q): The result of division. Remainder (A): What’s left after division.

## Slide 8
Start
n = no. of bits
M = Divisor
A = 0 (remainder)
Q = Dividend
Shift Left Q
A = A-M
A[n] ?
Q[0] = 0
Restore A
Q[0] = 1
n = n-1
n=0?
Quotient in Q
Remainder in A
Stop
= 1
= 0
No
Yes

## Slide 9: Binary Division Example: 11 ÷ 3
Dividend (Q) = 11 → 1011
Divisor (M) = 3 → 00011
(-M) = 11101
Remainder (A) = 0 → 00000 (initially)
Bit Length (n) = 4

## Slide 10
Step-by-Step Table for 11 ÷ 3 (Binary)
Step | A (5 bits) | Q (4 bits) | Operation | Action Taken
Init | 00000 | 1011 | — | Initialize A = 0
4 | 00001 | 011_ | Left shift A:Q | Shift AQ left by 1
 | 11110 | 011_ | A = A - M = 00001 + 11101 = 11110 | Negative → Restore, Q₀ = 0
 | 00001 | 0110 | A = A + M = 11110 + 00011 = 00001 | Restored A
3 | 00010 | 110_ | Left shift A:Q | Shift AQ left
 | 11111 | 110_ | A = A - M = 00010 + 11101 = 11111 | Negative → Restore, Q₀ = 0
 | 00010 | 1100 | A = A + M = 11111 + 00011 = 00010 | Restored A
2 | 00101 | 100_ | Left shift A:Q | Shift AQ left
 | 00010 | 1001 | A = A - M = 00101 + 11101 = 00010 | Positive → Q₀ = 1
1 | 00101 | 001_ | Left shift A:Q | Shift AQ left
 | 00010 | 0011 | A = A - M = 00101 +11101 = 00010 | Positive → Q₀ = 1
Result | Remainder = 2 | Quotient = 3 |  | 

## Slide 11: Hardware Design and Implementation
Digital Signal Processors (DSPs):
The Restoring Division Algorithm can be implemented in DSPs for basic arithmetic operations, especially in low-cost or low-power devices where simplicity and predictability are more important than speed.
Microcontrollers:
Many microcontrollers, particularly those designed for embedded systems with limited resources, use simpler algorithms like Restoring Division to perform division operations. These systems often prioritize cost-effectiveness and energy efficiency over raw computational speed.
Field-Programmable Gate Arrays (FPGAs):
In FPGA designs, the Restoring Division Algorithm can be implemented using basic logic gates and shift registers. Its step-by-step nature makes it easier to map onto hardware compared to more complex division algorithms.
Arithmetic Logic Units (ALUs):
Basic ALUs in simple processors or custom-designed chips may implement Restoring Division as part of their division operation capabilities. This is especially true for older or less complex architectures.

## Slide 12: Low-Power and Resource-Constrained Systems
Internet of Things (IoT) Devices: IoT devices often operate under strict power and resource constraints. Algorithms like Restoring Division, which require minimal hardware resources, are suitable for such environments where computational efficiency is secondary to power efficiency.
Wearable Devices: Similar to IoT devices, wearables like fitness trackers and smartwatches benefit from simple algorithms that minimize energy consumption while still enabling basic arithmetic operations.

## Slide 13: Verification and Testing
Hardware Verification: The Restoring Division Algorithm can serve as a reference implementation for verifying the correctness of more complex division algorithms or hardware units. Its predictable behavior makes it a reliable benchmark.
Simulation and Debugging: During the development of new processors or arithmetic units, the Restoring Division Algorithm can be used as a test case to ensure that the hardware correctly handles division operations.

## Slide 14: Conclusion
The Restoring Division Algorithm finds its niche in applications where simplicity, reliability, and low resource consumption are prioritized over speed. Its primary uses include hardware design (especially in FPGAs and microcontrollers). While modern systems often employ more sophisticated algorithms, the Restoring Division Algorithm remains a valuable tool for understanding and implementing basic binary division.